## Slide 1: National Traffic System Net Training
Week 4:
Traffic is Traffic

## Slide 2: Traffic is Traffic
Modes
Phone
CW
Digital

## Slide 3: Modes
The Three Modes
Phone (Voice) – HF or V/UHF
CW – HF
Digital – HF or V/UHF
The modes are interoperable: the Radiogram is unchanged!

## Slide 4: Traffic is Traffic
Modes
Phone
CW
Digital

## Slide 5: Phone
Resources
FSD-218
ARRL “Communicating with Other Hams”
Protocol
ITU Phonetic Alphabet
“I Spell”
“Mixed Group”
“Figures”
“Phone Figures”
“Initials”

## Slide 6: Phone
Example

## Slide 7: Traffic is Traffic
Modes
Phone
CW
Digital

## Slide 8: CW - Review
Resources
FSD-218
ARRL “Communicating with Other Hams”
Q-sigs, Abbreviation, Prosigns
QRV
QSL
-AA-
-AR-
-BT-
  N
  C
  B#
  QNX

## Slide 9: CW
Example

## Slide 10: Traffic is Traffic
Modes
Phone
CW
Digital

## Slide 11: Digital
Resources
WinLink
NTS-Digital.net
Protocol
Uses a text only version of the Radiogram
WinLink – Radiogram Form. Uses the Internet to WinLink nodes. Outgoing traffic only
MBO – Uses RF Only, VARA protocol. Can be used for outgoing and incoming traffic
NOTE: DO NOT MIX BOTH WINLINK AND MBO MESSAGES IN YOUR OUTBOX AND CONNECT TO EITHER TYPE OF NODE

## Slide 12: WinLink
Resources
WinLink
WinLink uses RF to WinLink nodes and then the Internet to an MBO
Select “RADIOGRAM” on a new message

## Slide 13: WinLink
A browser window opens with a Radiogram Form. Fill it out, select a Liaison Station and click Submit

## Slide 14: WinLink
The message is transferred to the WinLink message properly formatted and is ready to post to your outbox

## Slide 15: Mailbox Operation
Message ready to be sent to an MBO

## Slide 16: Mailbox Operation
Resources
WinLink
How to setup VARA to Access DTN Hubs
Western Area Guidelines and Stations
Summary
Address and Subject must be formatted correctly
The radiogram must be manually formatted correctly
Uses the VARA digital protocol
You must be set up in advance to receive traffic

## Slide 17: Wrap up
Questions?, Comments
Next Week- Introduction to CW Traffic Nets
V-Band Simulated Net
Net Class Manual