## Slide 1: National Traffic System Net Training
Week 5:
Checking into a CW Traffic Net

## Slide 2: Checking Into a CW Traffic Net
Q-Signal Review
Check in/out procedure
CSN Recording

## Slide 3: Q-Signal Review
Resource
FSD-218
Q-Signals, Prosigns, Abbreviations
QRL
QND
QNZ
QNA
QNI
QRU
QTC
-AR-
  HR
  QRV
  QSK
  QSL
  R
  QNX
  -SK-
  QNF
  -AS-

## Slide 4: Checking Into a CW Traffic Net
Q-Signal Review
Check in/out procedure
CSN Recording

## Slide 5: Check-in Procedure
Checking into a net
Net Control sends QNI K as an invitation for general check ins
To check in, send a single character, usually the first letter in your suffix
The NCS will send the letter of the station they want to QNI next
When the NCS sends your letter, check in by sending DE –call- GE -NCS name- QRU –AR- if you have no traffic
The NCS will acknowledge your QNI

## Slide 6: Check-out Procedure
Checking out of a net
Net Control sends your call
Respond with R
The minimum response is something like TU LANE 73 DE W2ITT –SK-
The NCS will send something like W2ITT TU ROB FER QNI NW QNX 73 K
NOTE: once checked into a net don’t leave until the NCS checks you out

## Slide 7: Checking Into a CW Traffic Net
Q-Signal Review
Check in/out procedure
CSN Recording

## Slide 8: CSN Recording Preamble & Check in
Click for recording

## Slide 9: CSN Recording Passing Traffic
Click for recording

## Slide 10: CSN Recording Checking out & Ending the net
Click for recording

## Slide 11: Wrap up
Questions?, Comments
Next Week- The Next Level
V-Band Simulated Net
Net Class Manual